## Slide 1: UVM for K Means IP
Project by:
Liora Huf
Eddy Sraiber
Supervised by:
Goel Samuel

## Slide 2: Content
Hardware Verification
UVM
DUT
Implemented UVM Environment
Test Plan
Tests Results
Bug Fixes
Coverage Results
Summary and Conclusion

## Slide 3: Hardware Verification
Ensure that the devices performs this task successfully,
  the device is an accurate representation of the specification.
  Bugs are only the result of the discrepancy between the device design and the device specification.
Design verification (DV) contains different technologies, languages, and methodologies:
  UVM (Universal Verification Methodology)
  UPF (Unified Power Format) low-power verification
  AMS (analog/mixed signal) verification
In this project, the chosen design verification method was UVM

## Slide 4: UVM
The primary advantage of the UVM is that it specifies and lays out a set of guidelines to be followed for creation of verification testbenches. This fact ensures:
  testbench uniformity between different verification teams
  cross-compatibility between IPs
  standalone environment integration
  flexibility and ease of maintaining testbenches.
Every verification environment has similar components like drivers, monitors, transactions and scoreboards.
UVM provides a build in base class for each of these components with standardized functions to instantiate, connect and build the test bench environment.
Notes: The primary advantage of the UVM is that this methodology specifies and lays out a set of guidelines to be followed for creation of verification testbenches. This fact ensures testbench uniformity between different verification teams, cross-compatibility between IPs and standalone environment integration, as well as flexibility and ease of maintaining testbenches.
Every verification environment has similar components like drivers, monitors, stimulus generators and scoreboards. UVM provides a build in base class for each of these components with standardized functions to instantiate, connect and build the test bench environment.

## Slide 5: UVM Structure
The UVM usual structure is constructed with the following classes:
Top block
Sequence
Sequencer
Driver
Monitor
Agent
Scoreboard
Env
Test

## Slide 6: UVM Structure- Top block
The top block is responsible for:
Create instances of the DUT, the Reference model and of the testbench.
Declare the virtual interface, which will act as a bridge between the Test component and the DUT/Reference Model.(The interface is a module that holds all the signals of the DUT. The monitor, the driver and the DUT are all going to be connected to this module.)
Connecting the DUT and Reference Model to the test class, using the interface defined before.
Generating the clock for the DUT.
Registering the interface in the UVM factory. (This is necessary in order to pass this interface to all other classes that will be instantiated in the testbench. )
Running the test.
Notes: The top block will create instances of the DUT, the Reference model and of the testbench. It will also declare the virtual interface, which will act as a bridge between the Test component and the DUT/Reference Model.
The interface is a module that holds all the signals of the DUT. The monitor, the driver and the DUT are all going to be connected to this module.
This block will be a typical SystemVerilog module and it will be responsible for:
  Connecting the DUT and Reference Model to the test class, using the interface defined before.
  Generating the clock for the DUT.
  Registering the interface in the UVM factory. This is necessary in order to pass this interface to all other classes that will be instantiated in the testbench. It will be registered in the UVM factory by using the uvm_resource_db method and every block that will use the same interface, will need to get it by calling the same method.
  Running the test.

## Slide 7: UVM Structure - Test
This block is derived from the uvm_test class and it will have two purposes:
  Create the env block
  Connect the sequencer to the sequence
The sequencer and the sequence are connected in this block, instead of the agent block or the sequence block because by specifying in the test class which sequence is going to be generated in the sequencer, the kind of data is transmitted to the DUT can be easily changed, without any change in the agent’s or sequence’s code.

## Slide 8: UVM Structure- Sequence & Sequencer
A transaction is a class object, usually extended from uvm_transaction or uvm_sequence_item classes, which includes the information needed to model the communication between two or more components.
Sequences are an ordered collection of transactions, they shape transactions to our needs and generate as many as we want.
The sequencer transfers one transaction at the time from the sequence to the driver

## Slide 9: UVM Structure - Env
The env is a very simple class that instantiates the agent and the scoreboard and connects them together.

## Slide 10: UVM Structure-Driver
The driver is a block whose role is to interact with the DUT.
The driver pulls transactions from the sequencer and sends them repetitively to the signal-level interface. This interaction will be observed and evaluated by another block, the monitor, and as a result, the driver’s functionality should only be limited to sending the necessary data to the DUT.

## Slide 11: UVM Structure-Monitor
The monitor observes the communication of the DUT with the testbench.
The monitor is a passive component, it doesn’t drive any signals into the DUT, its purpose is to extract signal information and translate it into meaningful information to be evaluated by other components.
A verification environment is not limited to just one monitor, it can have multiple monitors. In the case of this project, the environment will have two monitors: one for the DUT and one for the Reference Model.
The monitors should cover the outputs of the DUT/Reference Model in order to later send them to the scoreboard.

## Slide 12: UVM Structure-Agent
The purpose of the agent module is:
Construct the monitors, the sequencer and the driver in the build phase.
Create two analysis ports, these ports will act as proxies for the monitors to be connect to an external scoreboard through the agent’s ports. Using the concept of TLM ports, it can connect each port to its destination.
Connect both monitors, the sequencer and the Driver.
Notes: The purpose of the agent module is to connect both monitors, the sequencer and the driver. An agent doesn’t require a run phase, there is no simulation code to be executed in this block but there will be a connect phase, in addition to the build phase.
The Agent component will construct the monitors, the sequencer and the driver in the build phase. It will also need to create two analysis ports, these ports will act as proxies for the monitors to be connect to an external scoreboard through the agent’s ports.
After it has constructed the components previously mentioned , the Agent has to make the connections between them. Using the concept of TLM ports, it can connect each port to its destination.

## Slide 13: UVM Structure-Scoreboard
The scoreboard verifies the proper operation of a design at a functional level.
In this project, the same inputs are driven into the DUT and into the Reference Model, and their outputs are monitored by the monitors. The scoreboard then receives these outputs and compares them.
There are designers who prefer to leave the prediction to the scoreboard. So, the functionality of the scoreboard is very subjective.
In the agent, two monitors were created, as a result, two analysis exports had to be created in the scoreboard, which are used to retrieve transactions from both monitors.
A method compare() is executed in the run phase to compare both transactions. If they match, it means that the Reference Model and the DUT both agree on the functionality and it will return an “OK” message.

## Slide 14: DUT – The K means algorithm
Given the cluster number K, the K-means algorithm is carried out in 4 steps:
Initialization: randomly setting the initial centroids.
Classification: assign each object to the cluster with the nearest centroid measured with a specific distance metric.
Centroid update: Compute new centroids of the clusters given the current partition.
Convergence check: Compare new centroids to the ones from last iteration:
  If they “close” to each other (their norm difference does not proceed predetermined threshold), end the algorithm.
  Else, start another iteration by returning to Classification step with the new centroids.

## Slide 15: DUT - Architecture
The high-level architecture composed of two main modules - The “Register file” and the “K means core”.
The “Register file” – communication mediator:
  Communicate with the CPU host by APB protocol, as APB slave, and store income data.
  Communicate with “K means core”, and store output data as well as during algorithm data such as cluster centroids, by allowing read and write to its registers.
The “K means core” module – the “brain”.
  Run the algorithm, when finished – throw an interrupt to CPU host (passed through the “Register file”).
  Include a local RAM for restoration of the data set , the data is written to it through the “Register file”, by APB protocol as mentioned above

## Slide 16: DUT - Input data characteristics
Every data in the DUT is a seven-dimensional point.
Every data point coordinate or centroid coordinate in the DUT is represented by fixed point representation with 13 bits: 1(the MSB is the sign bit),2 for the integral part of the number and 10 for the fractional part of the number.
Therefore, every data coordinate a dynamic range of [-3.999,3.999]
The data points are stored in the DUT as matrix of 512X7
In the worst case where all data points enter the same accumulator, the accumulator maximum value per coordinate will be as high as:
In order to represent this value, 22 bits will be needed: 1(the MSB is a sign bit), 11 for integer part of the number and 10 for the fractional part of the number.

## Slide 17: DUT - Parameters
Before setting the “Go” register to 1, at least 8 data points need to be written to the IP’s RAM.
Before setting the “Go” register to 1, the following registers need to be configured (not necessarily in this order):
  First ram addr
  Last ram addr
After performing these configurations, in order to instruct the DUT to start its function, the user must write the value ‘1’ to register named “Go_reg”.
The default value for all centroid initial is zero.The centroid initial values can be configured by writing these values to registers “Cent_X_reg”(X is an integer between 1 and 8).
The threshold value used for convergence check of the algorithm may be configured by user. It can be configured by writing the desired threshold value to register “Thresh hold”. The default value for threshold is zero.
Notes: Before setting the “Go” register to 1, at least 8 data points need to be written to the IP’s RAM. The maximum Ram capacity is 512 data points, therefore, insertion of more than 512 data points may cause unexpected behavior.
Before setting the “Go” register to 1, the following registers need to be configured (not necessarily in this order):
  First ram addr – this register must be configured to the first ram address in which the user wrote data.
  Last ram addr - this register must be configured to the last ram address in which the user wrote data.
The maximum Ram capacity is of 512 data points, therefore the parameter “First ram addr” should be between 1 and 512. The parameters “Last ram addr” shall therefore be set to the sum of the parameter “First ram addr” and the number of points chosen by the user.
After performing the configurations described above, in order to instruct the DUT to start its function, the user must write the value ‘1’ to register named “Go_reg”.
The centroid initial values can be configured by writing these values to registers “Cent_X_reg”(X is an integer between 1 and 8),before the “Go_reg” is configured to ‘1’. In case these registers are not configured, all centroid initial values will be set to zero.
The threshold value used for convergence check of the algorithm may be configured by user. It can be configured by writing the desired threshold value to register “Thresh hold”. In case this register is not configured, the threshold value will be set to zero.

## Slide 18: Implemented Environment - Transaction
The transaction used by the verification environment was named Kmeans_transaction. It is a class is derived from of the UVM built in class uvm_sequence_item and has the following variables and constraints:
Variable name | Type | Constrain | Purpose
Centroids | Rand logic [8][91] |  | Used to randomly generate initial centroid values for DUT and ref model
Num_points | Rand int | 8<num_points<512 | Used to randomly generate the number of points used as input points on the DUT and on the ref Model
Data_points | rand logic [512][91] |  | Used to randomly generate data points values for DUT and ref model
Threshold | rand logic [12:0] | threshold[12:8] == 5'd0 (so the threshold is small) | Used to randomly generate threshold value for DUT and ref model
first_point_index | rand logic [13] | first_point_index <= 512 - num_points; first_point_index >=1; | Used to randomly generate the RAM index where the first data point will be stored
last_point_index | Rand logic [13] | last_point_index == num_points + first_point_index - 13'b1 | Used to randomly generate the RAM index where the last data point will be stored

## Slide 19: Implemented Environment - Sequence
The sequence class used by the verification environment was named Kmeans_in_sequence.
It is a class is derived from the UVM built in class uvm_sequence .
In Kmeans_in_sequence:
  Variable called num_txs which is set to be the number of transactions the Testbench will produce and send
  a loop which runs num_txs times. Each iteration,a Kmeans_transaction is instantiated, and the function randomize is called to generate all variables which are “rand” type in the K means transaction.
  The Instantiated transaction is then sent to the driver with the function start_item(thorught the sequencer)
  When the driver finishes the transaction , the sequence ends this transaction with the function finish_item .

## Slide 20: Implemented Environment - Driver
The Driver class used in the environment was named Kmeans_driver and it is a class is derived from the UVM built in class uvm_driver.
As the driver is responsible for sending the transaction (Kmeans_trasaction) to the DUT and the Ref model, it implements the following tasks:

## Slide 21: Implemented Environment - Scoreboard
The Scoreboard implemented class contains:
  Two uvm_analysis_export (one for the DUT centroids and one for the Ref Model centroids)
  Two uvm_tlm_analysis_fifo (one for the DUT centroids and one for the Ref Model centroids)
  Virtual functional named compare centroids
In is Run task, the Scoreboard class calls the function compare_centroids in order to determine if a test run failed or passed.
This function determines the result by comparing the centroids od the DUT and the Ref Model, if the overall difference between all coordinates off all centroids is smaller than 16 times the value of the threshold.
The pass/fail condition was derived from the functionality of the DUT and Ref Model, which consider a centroid converged if the absolute value of the distance between it and the last iteration centroid is smaller than the threshold value.
Notes: The Scoreboard implemented class contains:
  Two uvm_analysis_export (one for the DUT centroids and one for the Ref Model centroids)
  Two uvm_tlm_analysis_fifo (one for the DUT centroids and one for the Ref Model centroids)
  Virtual functional named compare centroids
This class uses the uvm_tlm_analysis_fifo and uvm_analysis_export in order to get the results from the DUT and Ref Model (the eight centroids of each of them).
In is Run task, the Scoreboard class calls the function compare_centroids in order to determine if a test run failed or passed.
This function determines the result by comparing the centroids od the DUT and the Ref Model, if the overall difference between all coordinates off all centroids is smaller than 16 times the value of the threshold. The pass/fail condition was derived from the functionality of the DUT and Ref Model, which consider a centroid converged if the absolute value of the distance between it and the last iteration centroid is smaller than the threshold value.

## Slide 22: Implemented Environment – Reference Model
The Reference Model used to check the DUT results was written using Matlab. It is Matlab function named RefModel.m. This functions implements the K Means algorithm in software.
The RefModel.m function receives five input parameters:
  Point input matrix with 512 rows and 7 columns, where each row represent a point in the DUT numeric representation model
  Initial centroid matrix with 8 rows and 7 columns, where each row represents an initial centroid value in the DUT numeric representation model.
  Input threshold value in the DUT numeric representation model
  First point index
  Last point index
Notes: The Reference Model used to check the DUT results was written using Matlab. It is Matlab function named RefModel.m. This functions implements the K Means algorithm in software.
The RefModel.m function receives five input parameters:
  Point input matrix with 512 rows and 7 columns, where each row represent a point in the DUT numeric representation model, i.e. each row is a point with 7 dimensions, each dimension is a fixed point number with 13 bits(MSB is the sign bit, the following two bits represent the integer value and the remaining ten bits represent the fractional part)
  Initial centroid matrix with 8 rows and 7 columns, where each row represents an initial centroid value in the DUT numeric representation model.
  Input threshold value in the DUT numeric representation model
  First point index
  Last point index

## Slide 23: Implemented Environment – Reference Model
These parameters are used in the following way: the Reference model function reads the points values from the “First point index” till the “Last point index” into another matrix, named point matrix , which will be used to run the algorithm.
Then the function interactively executes the algorithm using the point matrix, the “input centroid matrix” and the “input threshold”.
The following figure summarizes the Reference Model in a flow chart:
Notes: These parameters are used in the following way: the Reference model function uses the Point input matrix as the DUT uses its RAM, it read the points values from the “First point index” till the “Last point index” into another matrix, named point matrix , which will be used to run the algorithm.
Then the function interactively executes the algorithm using the point matrix, the “input centroid matrix” and the “input threshold”.
The following figure summarizes the Reference Model in a flow chart:

## Slide 24: Test Plan – Verifying APB Protocol
In order to verify the functionality of the communication with the DUT, an early test was done in which all registers of the DUT Reg File were written to and read from. This test was successful, leading to the conclusion that the communication protocol with the DUT works correctly.

## Slide 25: Test Plan – Test Scenarios
Each Test Scenario detail here was built and run. The purpose of these test lines is to test the main functionality of the DUT and not the communications protocol.
For each test, the pass/fail criteria is as described in the Scoreboard class.
In each test scenario, different parameters are set .These parameters are sent to the DUT and the REF Model. The outputs given by the DUT and the REF Model for the mentioned input are compared. They are considered equivalent if every output centroid presented by the DUT is also presented by the REF Model.

## Slide 26: Test Plan – Test Scenarios
Test Scenario Number | Test Scenario Name | Random Generated Paraments | Constrains
1 | Gradual Random Points | Centroids one to eight Threshold value will be one Ten data points. | Centroids one to eight will be set to values 1 to 8(respectively) Threshold value will be one (only threshold LSB will be one). First only one data point will be random.At each iteration, one more data point will be randomly generated.
2 | One Iteration Test | 1. Eight values | These eight values will be used both as points values and initial centroid values.
3 | Random Points and Centroids | Eight Points values Eighth initial Centroid values | Eight Points values will be randomly generated Eighth initial Centroid values will be randomly generated

## Slide 27: Test Plan – Test Scenarios
Test Scenario Number | Test Scenario Name | Random Generated Paraments | Constrains
4 | Random Constrained Number of Points | Number of points Points values Initial Centroid values | This test will be run overall ten times, where in each run the constraint over the Number of Points parameters will change.
5 | Equal Initial Values Test | Number of points Points values A single value which will be used as an initial value for all centroids. | 
6 | Positive Overflow Test | Initial Centroid values | 512 data points will be generated and set to have maximum allowed value.

## Slide 28: Test Plan – Test Scenarios
Test Scenario Number | Test Scenario Name | Random Generated Paraments | Constrains
7 | Negative Overflow Test | Initial Centroid values | 512 data points will be generated and set to have minimum allowed value.
8 | Full Memory Test | 512 points values Initial centroid values | 
9 | Fully Random Test | Number of points Points values Initial Centroid values | 

## Slide 29: Test Plan – Test Scenarios
Test Scenario Number | Test Scenario Name | Random Generated Paraments | Constrains
10 | Isolated Centroid Test | Number of points Points values Initial Centroid values | One of the centroids is constrained to be far away from the all the data points. All of the centroids, except from one, are constrained to be far away from the all the data points.
11 | Robustness Test | Number of points Points values Initial Centroid values | 
12 | Threshold Test | Number of points Points values Initial Centroid values Convergence threshold value | 

## Slide 30: Test Plan – Test Results
Test Scenario Number | Number of tests | Fail number | Fail Percent [%]
1 | 10000 | 23 | 0.23
2 | 10000 | 0 | 0
3 | 10000 | 4 | 0.4
4 | 11 | 4 | 36.36
5 | 10 | 5 | 50
6 | 10 | 0 | 0
7 | 10 | 0 | 0
8 | 10 | 9 | 90
9 | 10 | 3 | 30
10 | 10 | 6 | 60
11 | 10000 | 1941 | 19.41
12 | 10 | 0 | 0

## Slide 31: Bug Fixes - Negative values bug
While building the verification environment, a “sanity check test” done in order to verify if the UVM environments works, the results from the DUT indicated a bug. This bug was apparently connected related to the DUT’s inability to recognize negative values. This bug was fixed by the following steps:
  Fix sign representation of variables
  Fix 2's complement representation of numbers

## Slide 32: Bug Fixes - Combinatorial sensitivity list missing item
In convergence_check_block, the new calculated centroids of each iteration are checked for convergence by comparing them to the last iteration’s centroids values.
If convergence was not reached, the new centroids are used in the next iteration as the algorithm centroids.
In the convergence check module, there is a sensitivity list used to take one old centroid from the 8 and compare it to the correspondingly new centroid.
This sensitivity list did not cover the change in values of the relevant inputs for this supposedly combinatorial representation of always.
The following fix was done to solve the problem:
  Before: "always @(cent_num) begin".
  After: "always @* begin".
Notes: In convergence_check_block, the new calculated centroids of each iteration are checked for convergence by comparing them to the last iteration’s centroids values(one by one). In the case where convergence was not reached, the new centroids are used in the next iteration as the algorithm centroids.
In the convergence check module, there is a sensitivity list used to take one old centroid from the 8 and compare it to the correspondingly new centroid which come as input from prior module (new means calculation block).
This sensitivity list did not cover the change in values of the relevant inputs for this supposedly combinatorial representation of always, the following fix was done to solve the problem:
  Before: "always @(cent_num) begin".
  After: "always @* begin".

## Slide 33: Bug Fixes - Correction of the wrong controller signal toggle during state machine transitions, in the 2nd state of empty_pipe
The controller has a signal for enabling the accumulators of the pipe3 of classification block. The signal determines when to sample data point, which comes as input from the RAM to the classification block.
After the last data point reached the last pipe stage, no more data should be sample by the accumulators.
Therefore, the enable needs to be turned off so at that in the next state, there would be no sampling of any more data points.
The bug was that the DUT sampled one more data point then needed.
Disabling the enable signal one state/cycle earlier, removed the bug.
Notes: The controller has a signal for enabling the accumulators of the pipe3 of classification block. The signal is in charge of determining when to sample data point, which comes as input from the RAM to the classification block.
After the last data point reached the last pipe stage, no more data should be sample by the ccumulators(“garbage” data may be present in the pipe) . Therefore, there is a need to pull down the enable so at that in the next state, which is "calculate new means", there would be no sampling of any more data points.
There was a bug which we sampled one more data point since we pulled down the signal only at the "calculate new means" state. Pulling it down one state/cycle earlier, removed the bug.

## Slide 34: Coverage results
Coverage was performed for the test line called Robustness because it is the most “random” test line(every input for the DUT is randomly generated) and it has the biggest number of tests.
The total coverage results can be seen in the following figure:

## Slide 35: Coverage results – Code Coverage
As can be seen from the attached figure,the total code coverage was 91.43%.The following figure details the code coverage from the DUT modules:

## Slide 36: Coverage results – Functional Coverage
In order to check the functional coverage of the test line, the following cover groups were defined:
  NUM_POINTS - Samples the number of data , to verify that all values of this variable are uniformly distributed between 8 and 512.
  DATA_VALUE – Samples the values of each one of the seven coordinates of all data points ,to verify that all values of this variable are uniformly distributed between all the possible values.
  CENTX_VALUE - Samples the value of each one of the seven coordinates of centroid X,to verify that all values of this variable are uniformly distributed between all the possible values.
Notes: In order to check the functional coverage of the test line, the following cover groups were defined:
  NUM_POINTS - This cover group samples the number of data points randomly generated for each test, to verify that all values of this variable are uniformly distributed between 8 and 512.
  DATA_VALUE - This cover group samples the values of each one of the seven coordinates of all data points randomly generated for each test, to verify that all values of this variable are uniformly distributed between all the possible values.
  CENTX_VALUE - This cover group samples the value of each one of the seven coordinates of centroid X, randomly generated at each test, to verify that all values of this variable are uniformly distributed between all the possible values.

## Slide 37: Coverage results – Functional Coverage NUM_POINST
As can be seen form the figures attached, the number of points in all the tests was uniformly distributed between 8 and 512.

## Slide 38: Coverage results – Functional Coverage DATA_VALUE
As can be seen form the figures attached, for all data points, the values of their coordinates were normally distributed between all the possible values in all the tests.

## Slide 39: Coverage results – Functional Coverage CENT_VALUE
As can be seen form the figure attached, for centroid 1 the values of its coordinates were normally distributed between all the possible values in all the tests. This also is correct for the other 7 centroids.

## Slide 40: Coverage results – FSM Coverage
The default FSM coverage has a low result because it checks all transitions for the FSM, even the ones which are not legal.
Therefore, a cover group for the legal transitions was built.
The FSM present in the DUT is the one inside the controller module.
The cover group for the valid transitions was written according to the transitions and control signals in the following figure, which describes the K means controller FSM:

## Slide 41: Coverage results – FSM Coverage
The FSM states were named according to the following table:
Idle | S0
Read centroid | S1
Write centroid | S2
Read first point Ram | S3
Fill pipe | S4
Classify remaining points | S5
Empty pipe1 | S6
Empty pipe 2 | S7
Calculate new mean | S8
New centroid write & convergence check | S9
Write new centroid to Reg File | S10
Interrupt | S11

## Slide 42: Coverage results – FSM Coverage
The states coverage was of 100%, as it can be seen in the following figures:

## Slide 43: Summary & Conclusions
The tests results indicate that are still bugs in the DUT, which we were not able to find and fix.
The high fail rate in test line 8 indicates that there is an overflow bug when trying to fill the RAMs.
Test line 3 and 4 indicate that as the number of data points increases so does the number of fails. This could be related to bugs such as overflow, wrong classification of close points, and/or wrong calculations.
Even though many test benches were run on the DUT in its design phase, many tests have failed. This emphasizes the need for an efficient verification environment, as UVM, parallel to the design process.
UVM is an effective tool. It is intuitive, with high level coding and easy to reuse, making the verification process simpler and faster.
Notes: The tests results indicate that are still bugs in the DUT, which we were not able to find and fix. If the DUT was a commercial IP, we would advise the company to do a thorough debugging process.
The high fail rate in test line 8 indicates that there is an overflow bug when trying to fill the RAMs.
Test line 3 and 4 indicate that as the number of data points increases so does the number of fails. This could be related to bugs such as overflow, wrong classification of close points, and/or wrong calculations.
Even though many test benches were run on the DUT in its design phase, many tests have failed. This emphasizes the need for an efficient verification environment, as UVM, parallel to the design process.
UVM is an effective tool. It is intuitive, with high level coding and easy to reuse, making the verification process simpler and faster.

## Slide 44: Thank you